IEEE 802.11 Wireless LAN  The MAC Layer
IEEE 802.11 Wireless LAN
The MAC Layer
Hal Feinstein
GD-AIS/Herndon

---
Talk Outline
Talk Outline
Introduction to the MAC Layer
Differences between wire and wireless
IEEE 802.11 MAC Layer Basics
Advanced 802.11 MAC Services
Developments and Future

---
IEEE 802.11 WLAN The Office Environment
IEEE 802.11 WLAN
The Office Environment
The environment:
  - An RF version of a small office Ethernet (WLAN)
  - It is not (or should not be) a WMAN
  - Optimized for the office environment
    - Many RF reflections
      - Broad signal strength variations
      - Many dead spots due to destructive interference.
    - Interference from nearby transmitters
      - ISM band is shared with others wireless networks and other unlicensed RF devices (example: wireless camera).
      - Three ISM bands are allocated for part 15 (unlicensed use)

---
Various Types of IEEE 802.11
Various Types of IEEE 802.11
* Proprietary solutions, draft standard only.
** Pure g devices, no b devices in cell
200+ 100
54 24 **
11 6
54 25
ChannelRate
Spec Measured
OFDM
2.3 Ghz
802.11g
OFDM
2.3 Ghz
802.11n*
DSSS
2.3 Ghz
802.11b
FHSS
5. Ghz
802.11a
Modulation
Band
Type

---
Similarities and Differences between Ethernet and RF Office Environment
Similarities and Differences
between Ethernet and RF Office Environment
Ethernet
  - Non-polled, distributed channel access strategy
  - Competition for transmission time on a single channel
  - Units can listen while transmitting to sense collision allowing efficient collision detection (CD) strategy.
  - Signal strength consistent and predictable over length of cable.
  - Minimal or low interference.
RF WLAN Office Environment
  - Non-polled, distributed channel access strategy.
  - Stations compete for transmission time on a single channel.
  - Stations are half-duplex and cannot listen while transmit. Collision Avoidance strategy (CA) not more efficient CD.
  - Signal strength variable and unpredictable, depending upon office geometry. Multiple “dead-spots” all nodes may not hear each other.
  - Shared radio media must tolerate interference from other WLANs and from consumer and industrial devices operating in same band.

---
Operating in a Shared Channel Other Services Lower Signal Quality
Operating in a Shared Channel
Other Services Lower Signal Quality
Carrier Sense Multiple Access (CSMA) a clear channel means an idle channel and permission to transmit
  - Interference is sensed as a busy channel
CSMA marks transmission error as a probable collision causing backoff and retransmission
  - Interference creates error in transmissions

---
Operating in a Shared Channel  Other Services Create Interference
Operating in a Shared Channel
Other Services Create Interference
RF Interference from adjacent 802.11 networks is called self-interference
A
Interference
1
B
3
2
 Nodes 1 and 2 are within radio range of node 3
Network A and B take transmission time away each other

---
MAC Layer Design  Sharing a Single rf Channel
MAC Layer Design
Sharing a Single rf Channel
Norm Abramson Aloha Network (1968)
  - Multiple nodes share a single channel.
  - Listen Before Transmit (LBT)
    - Wait for clear (idle) channel for at least one round trip time.
  - Collision Avoidance not Collision Detection
    - While transmitting a station cannot hear others transmit.
Claims good average throughput for all
    - Statistical Assumptions necessary for Performance.
      - Traffic will be bursty in nature
        - Distributed as a Poisson distribution
        - Not true of newer streaming types of traffic
        - Faster Media (usually) hides this problem!

---
802.11 CSMA Throughput Listen Interval prevent collision and tunes performance
802.11 CSMA Throughput
Listen Interval prevent collision and tunes performance
Short Interframe Space (SIFS)
10 usec
SIFS LISTEN
INTERVAL
A
C
K
IDLE
A
SIFS = maximum round trip propagation time +
receiver preamble synchronization +
equipment turn around time +
small safety interval time
A
B
Two node contention-based network

---
802.11 Wait Intervals A wait intervals establishes a priority of channel access
802.11 Wait Intervals
A wait intervals establishes a priority of channel access
Short Interframe Space (SIFS)
  - Minimum fixed wait for equipment turn around and RF propagation
  - Minimum wait for control packets (ACK, CTS, etc…)
Slot Time
  - Unit of delay for calculating the backoff (contention window).
Distributed Interframe Space (DIFS)
  - DIFS = SIFS + 2 x Slot Time.
  - Minimum delay for packets containing data.
  - Longer delay ensures control packets always reach AP first.
Contention Window (CW)
  - Time to wait after a sensing a collision or busy channel
  - Ranges between 1 and 1024 slot times for specific 802.11 MAC (a,b or g)
*802.11 is not a slotted system but calculation of the variable backoff (bo) after collision is treated as a slotted interval.

---
802.11  Wait Values
802.11 Wait Values
* 9uS (short slot time) optional, 20uS (long slot time) mixed network with 802.11a/g
50uS
10uS
20uS
802.11b
28uS
34uS
Distributed Interframe Spacing
10uS
16uS
Short Interframe Space
20uS
9uS*
9uS
Slot Time
802.11g
802.11a
Wait Times

---
Basic Data Exchange  Without Collision 802.11b Example Values
Basic Data Exchange
Without Collision
802.11b Example Values
DIFS
50us
BO
31-1024us
SIFS
10us
DIFS
BO
A (DATA)
B (ACK)
Two Way Handshake

---
Data Exchange Channel is in use
Data Exchange
Channel is in use
S
B
(ACK)
DIFS
BO
SIFS
Backoff
Contention WIndow
A
WAIT
CHANNEL BUSY
Data
C
ONE SLOT TIME
S
A (DATA)
B(ACK)
DIFS

---
Data Exchange Example of a Collision
Data Exchange
Example of a Collision
NEGATIVE
ACK TIMOUT
BACKOFF
BO
SIFS
NO
ACK!
NO
ACK!
BO
SIFS
WINNER
GOES FIRST!
Collision!
DIFS
A (DATA)
DIFS
B (DATA)
B (DATA)

---
Hidden Transmitter Problem Contention scheme require all stations to hear each other to sense a clear channel
Hidden Transmitter Problem
Contention scheme require all stations to hear each other to sense a clear channel
A and C cannot hear each other but B hears both
A
C
B

---
Hidden Transmitter Solved by RTS-CTS mechanism Reserve Channel Time so hidden transmitter can finish its transmission
Hidden Transmitter
Solved by RTS-CTS mechanism
Reserve Channel Time so hidden transmitter can finish its transmission
A
B
DIFS
BO
RTS
CTS
SIFS
ACK
DATA
SIFS
SIFS
Channel Reserved
Reserve is released
Both contain reserve time field
Four Way Handshake

---
Hidden Transmitter Hidden Transmitter hears RTS and/or CTS Both RTS and CTS have reserve time fields
Hidden Transmitter
Hidden Transmitter hears RTS and/or CTS
Both RTS and CTS have reserve time fields
RTS
CTS
METAL SHELVING
CTS
A
B
DIFS
BO
RTS
CTS
SIFS
ACK
DATA
SIFS
SIFS
Channel Reserved
Reserve is released
Both contain reserve time field

---
Hidden Transmitter In the Real World
Hidden Transmitter
In the Real World
802.11 has no way to sense that a hidden transmitter is present.
The RTS-CTS channel reserve instead is turned on for any packet of 1000 bytes or greater without regard to a hidden transmitter.
It uses up valuable channel time lowering the overall throughput for large packets.

---
Protection Mechanism 802.11a and g in same network
Protection Mechanism
802.11a and g in same network
802.11a and g compatible AP uses a protection trick to allow both client types to operate in a single network.
  - Normally an 802.11g AP communicates to other 802.11g stations.
  - If an 802.11b station is present it must stand by to avoid interfering with the shared channel.
A protection mechanism is used when an 802.11g AP communicates with an 802.11g STA.
The AP switches to 802.11b slower speed and sends a CTS (called a CTS-to-self) forcing all 802.11b stations to wait until the 802.11g transmission finishes.

---
802.11 Non-Contention Method Polling
802.11 Non-Contention Method
Polling
Goal is to support streaming and higher duty cycle traffic.
  - Only bursty or single shot transaction traffic fits contention.
  - VoIP and streaming requires assured transmission characteristics (quality of service). Polling is better way to manage this type of service.
802.11 Non-Contention Service organizes a portion of the channel time into a polled interval.
  - The AP manages the polling list and buffers traffic until it can be delivered to the client.
This protocol mechanism is not implemented by any vendor.

---
802.11 Non-Contention Method: Polling Time Share between Polling & Contention
802.11 Non-Contention Method: Polling
Time Share between Polling & Contention
REPETITION PERIOD
Contention Free
(POLLING)
Contention Period
TRANSMIT
 BEACON
MSG SIGNALLING
END OF POLLING PERIOD
POLLING MANAGED BY ACCESS POINT (AP)

---
802.11 Non-Contention Method: Polling Streaming traffic better handled by polling
802.11 Non-Contention Method: Polling
Streaming traffic better handled by polling
POLL + DATA
ACK + DATA
Polling Period End Signal
PIFS
SIFS
CF
END
POLL
1
POLL
3
DATA
BEACON
1
DATA
3
ACK
Timeout
PIFS
30uS
ACK
POLL
2
ACK
DATA

---
802.11 Non-Contention Method Polling
802.11 Non-Contention Method
Polling
Although it is part of the 802.11 standard the Non-contention (Polling) Point Control Function (PCF) is not implemented by any vendor.
IEEE 802.11e will support QoS by adding enhancements to the DCF MAC layer such as longer delays.
  - Main mover here is VoIP over 802.11.

---
Distance of an 802.11b Link Point-to-Point
Distance of an 802.11b Link
Point-to-Point
802.11 is tuned to have optimal throughput up to a certain maximum distance.
In practice a point-to-point link depends on the timeout limit set for the SIFS and DIFS. Using 60uS-70uS as a guide:
  - RF travels at 975ft/uS.
    - In 60uS it travels approximately 11 miles.
    - In 70uS it travels approximately 13 miles.
  - A point-to-point link whose ends are 11 or 12 miles apart will operate optimally since the ACK is received w/o timeout.
  - Longer distances can also work but timeouts will occur.
    - Timeouts are treated as lost packets and the CA mechanism handles them as a potential collision triggering a backoff wait.
    - A link will still operate at these longer distances but throughput will be much lower.

---
Operating Distances for 802.11b
Operating Distances for 802.11b
IEEE 802.11b Ranges (Some maximums)
  - Design goal: 300 meters range in a office or factory. Greater distance can be achieved using multiple access points in a cell structure.
  - Not Untypical: a 10 mile point-to-point link with directional antennas and amplifiers.
  - Best Ever: a 40 mile point-to-point link across the desert with large parabolic antennas.
  - Rumors: Even father with smaller antennas

---
802.11 Battery Saver Feature Power Management
802.11 Battery Saver Feature
Power Management
Personal wireless devices depend upon battery power.
  - Transmitter on is very expensive, reception is expensive.
  - Sleep mode
    - Turn off all unnecessary circuits including receiver.
Device must periodically listen for pending traffic
  - Several approaches have been tried but none are optimal in reducing battery drain in all cases.
802.11 uses two different mechanisms.

---
802.11 Battery Saver Feature Two ways to receive data in sleep mode
802.11 Battery Saver Feature
Two ways to receive data in sleep mode
Wake up if traffic pending
Stay asleep in immediate mode
Send Single Frame Only
AP
BEACON
ACK
DATA
Null
Data
Frame
Null
Data
Frame
ACTIVE
SLEEP
Client 1
WAKE UP
PS BIT OFF
GO TO SLEEP
PS BIT IS SET
POLL
PS
Client 2
ACTIVE
SLEEP
SLEEP

---
Multicast Engineering Issues
Multicast
Engineering Issues
Reliability
  - Positive acknowledgement cannot be received from all members
Wakeup
  - A multicast transmission requires groups of clients to wake wasting batteries
  - Many multicast are queries directed to a single client but the exact client is not known (Example: TCP/IP ARP)
Lowers Channel Rate
  - Many multicasts lower available channel time for normal communications.
Additional Protocol Structures
  - Multicast group address, state-machine, “half-reliability”

---
802.11 support for multicast
802.11 support for multicast
DTIM = # BEACONS
Between xmissions
Multicast Data frame
(broadcast)
AP
BEACON
BEACON
Multicast Data frame
(broadcast)
Client 1
Each DTIM Interval AP broadcasts queued
Multicast and broadcast frames
Client sends UNICAST frame to AP
For broadcast to group address

---
802.11 beacon frame What is in a beacon frame?
802.11 beacon frame
What is in a beacon frame?
BEACON Interval
  - Time between beacon transmissions (.1 second typical)
Access Point Synchronization Timestamp
  - Synchronizes all processes associated with this AP
Service Set ID (SSID)
  - Network identifier, required for a station to join the BSS. It is not (nor ever was) intended to be secret.
List of supported access rates.
Physical Layer Parameters
  - Hope rate (802.11a), channel (802.11b)…..
Feature set a station must support to join network.
Traffic Indicator Map (TIM)
  - Identifies stations in power saver mode with pending traffic.

---
802.11  Roaming/Mobile
802.11
Roaming/Mobile
Support for Limited Roaming (Portable)
  - Multiple overlapping BSS form ESS with same SSID
  - Reconnection not supported by layer 3 which is localized.
Full Mobile Operations requires many new protocol mechanisms.
  - IEEE 802.11f “InterAccess Point Protocol”
    - Supports operation among an ESS.
    - Ignores layer 3 issues which dominate.
    - Proprietary one-vendor solutions (CISCO).
Who else?
  - Mobile IP (a design rfc, not implemented)
  - IPv6 contains mobile/roaming mechanisms already.

---
802.11 Security
802.11 Security
Original Wire Equivalent Privacy (WEP) had very bad luck
  - No cipher system can stand either bad design or bad luck. WEP has both.
    - Bad Design Example:
    - WEP protects user plaintext by generating a key stream using the RC4 cipher. The plaintext and key stream are XOR’ed to form ciphertext. 802.11 uses a CRC to protect against alterations. The way the cipher text is formed and the CRC are linear operations. Linear operations allow the plaintext to be manipulated in meaningful ways through the encryption. The CRC can be altered using similar linear operations to make these changes undetectable.
    - Bad Luck Example:
    - WEP creates a key by concatenating the IV to a short key to form a longer key. The IV is assumed public, the key private. This technique is a well known and is used successfully by other systems. When used with RC4 the concatenated key leads to an unanticipated exploitable weakness peculiar to RC4 where the unknown portion of the key is easily recovered. This is bad luck: other ciphers, using the same split key construct as WEP, are secure while RC4 is not.

---
802.11 Security
Unlike wired systems there is no physical boundary to enclose an RF system. Anyone so equipped can intercept the RF. Encryption is required to ensure confidentiality, but all transmissions are fully visible.
IEEE 802.11 designed around open security architecture model
IEEE 802.11i “Security”
  - WiFi WPA 1 make the best of what weve got.
  - WiFI WPA 2 new, based on strong practices, uses AES*
  - The Open System Architecture is retained
    - Control messages are still unauthenticated and unprotected

---
Various 802.11g  and b formats  in current use
Various 802.11g and b formats
in current use
Modulation Type
Transmission Scheme
Rate (MBPS)
BPSK
DSSS
1
QPSK
DSSS
2
CCK
DSSS
5.5
BPSK
OFDM
6
BPSK3
OFDM
9
CCK2
DSSS
11
QPSK
OFDM
12
QPSK1
OFDM
18
16 QAM
OFDM
24
16 QAM
OFDM
36
64 QAM
OFDM
48
64 QAM
OFDM
54

---
End    Thank You
End
Thank You